## Slide 1
Wireless Power by Resonant Magnetic Coupling
Chittharanjan S · Deekshitha R · Dani Firas Payyanakadavan
Department of Electrical Engineering, IIT Madras · EE2025 Engineering Electromagnetics
2 Executive Summary
Two identical 10-turn, 10 cm air-core spiral coils, series-tuned to 500 kHz, transfer power across a 1–10 cm gap with no wire between them. At 500 kHz the wavelength is 600 m, so the coils interact through the reactive near field: primary current creates a magnetic field (Ampère), part of its flux links the secondary (mutual inductance M), and Faraday's law induces the secondary voltage. Resonance cancels the coil reactance, so performance is set by coupling k and quality factor Q = 118.3. A Neumann-integral model gives k falling from 0.51 at 1 cm to 0.030 at 10 cm. A phasor circuit model, confirmed by closed-form theory and LTspice, predicts maximum efficiencies of 97 % at 1 cm, 86 % at 5 cm and 57 % at 10 cm. With the 6 Ω load (optimal at 5 cm), delivered power peaks at critical coupling (6.4 W near 9.75 cm), not where efficiency is highest. All results are analytical and simulated.
3 The Physical Concept
Why it matters. Wireless charging already powers phones, toothbrushes and medical implants, and is being scaled up for electric vehicles. With no plugs or contacts, a device can be sealed, waterproof, or inside the body. We study the core of it: two identical 10 cm coils, 1 to 10 cm apart, at 500 kHz.
How it works. An alternating current in coil 1 makes a magnetic field. Part of that field passes through coil 2 and, because it changes, induces a voltage there (Faraday's law). A capacitor in series with each coil makes it resonate: energy sloshes between the coil's magnetic field and the capacitor's electric field, so a small drive builds a large current. Both coils are tuned to the same f0, so energy passes from one to the other and the load RL takes it out.
Why it is short range. Each coil is 1/6000 of the 600 m wavelength, so it hardly radiates: the field is stored close to the coils. The coupling k falls from 0.51 at 1 cm to 0.03 at 10 cm, and like 1/d3 further out.
Left: field lines of coil 1, computed for our coils at d = 3 cm; wine lines thread coil 2 and set M. Right: the series-series circuit.
4 Governing EM Physics
(1) ∇ × H = J + ∂D/∂t ≈ J (k0a = ωa/c ≈ 5 × 10−4)
Ampère, quasi-static: the coil is 1/6000 of λ = 600 m, so displacement current is negligible.
(2) ∮ E·dl = −dΦ/dt ⇒ V2 = −jωM I1
Faraday: the changing shared flux induces the EMF that drives coil 2.
(3) Bz = μ0NIa2 / [2(a2 + z2)3/2]
M = Φ21/I1 = (μ0/4π) ∮∮ dl1·dl2 / r
Biot–Savart, Neumann: flux of coil 1 through coil 2 per amp. Pure geometry; M12 = M21.
(4) k = M/√(L1L2), k ∝ 1/d3 for d ≫ a
Coupling: ours is 0.513, 0.111, 0.030 at 1, 5, 10 cm; 1/d3 only for d ≳ 4a.
(5) f0 = 1/(2π√(LC)), Q = ω0L/R, f± = f0/√(1 ± k)
Resonance: 17.13 µH, 5.915 nF → 500 kHz; Q = 118.3 at 0.455 Ω. Strong k splits the peak.
(6) Z1I1 + jωM I2 = Vs, jωM I1 + Z2I2 = 0
Zin = R1 + ω02M2/(R2 + RL) at f0
Circuit, Poynting: at f0, Wm = We in each coil, so the source sees only resistance.
(7) ηmax = x / (1 + √(1 + x))2, x = k2Q1Q2
Efficiency: at RL = R2√(1 + x). At 5 cm x = 173, ηmax = 85.9 %, RL = 6.0 Ω.
(8) δ = √(2/(ωμ0σ)) = 0.094 mm (Cu, 500 kHz)
Skin depth: current crowds into a skin thinner than the 0.35 mm wire radius, raising R.
Boundary conditions: n̂·(B1 − B2) = 0, n̂ × (H1 − H2) = K. Metal forces Bn ≈ 0 (eddy currents): L, k fall and an Al plate 10 mm away adds 87 mΩ. Ferrite guides flux, raising k.
Symbols: N turns, a coil radius, d spacing; I1, I2 into the dots; Zi = Ri + jωLi + 1/(jωCi), RL added in Z2; σ conductivity; μ0 = 4π × 10−7 H/m.
5 Analysis and Simulation
Closed form and Neumann agree to ≤ 0.05 % (0.5–15 cm); k ∝ 1/d3 only for d ≫ a.
ηmax is 97 % at 1 cm, 86 % at 5 cm, 57 % at 10 cm; the fixed 6 Ω load gives 44 % at 10 cm.
At 2 and 5 cm the power peak splits in two; at 10 cm a single sharp peak sits at f0.
The best load RL,opt = R2√(1+x) moves with spacing; 6 Ω is best only at 5 cm.
5 Analysis and Simulation (cont.)
Setup
Planar spiral, N = 10
dout = 100 mm
wire 0.7 mm, pitch 1.0 mm
L = 17.13 µH, C = 5.915 nF
f0 = 500 kHz
R = 0.455 Ω, Q = 118.3
RL = 6.0 Ω
Vs = 5 V peak, Rs = 0
6 Demonstration: Model vs Model
7 Conclusion and References
|B| (µT) in the x–z plane: primary at 1 A, coil 2 at d = 3 cm.
• Validation chain: closed form ↔ Python Neumann sum + 2 × 2 phasor solver ↔ LTspice sim/wpt.asc. LTspice agrees with the solver to 5 × 10−10 % (2, 5, 10 cm, 350–650 kHz).
• Faraday in time: at f0, V2 = −jωMI1 and Z2 = R2 + RL is real, so i2 lags i1 by 90° (T0/4 = 0.50 µs).
• Light-load peaks f± (eq. 5) give k within 0.3 % at 1, 2, 5 cm (5 cm: 474.4 / 530.3 kHz → 0.1109).
• Finding: a 6 Ω load pulls them in (5 cm: 483.5 / 519.6 kHz → k = 0.072, 35 % low; 10 cm: 1 peak).
d (cm) | M (µH) | k | ηmax (RL,opt) | η at 6 Ω | PL at 6 Ω (W) | Regime
1 | 8.79 | 0.513 | 96.8 % (27.6 Ω) | 92.6 % | 0.098 | over-coupled
3 | 3.72 | 0.217 | 92.5 % (11.7 Ω) | 91.0 % | 0.526 | over-coupled
5 | 1.90 | 0.111 | 85.9 % (6.00 Ω) | 85.9 % | 1.79 | over-coupled; design point
10 | 0.51 | 0.030 | 57.2 % (1.67 Ω) | 43.5 % | 6.36 | near critical (k < kc)
Vs = 5 V pk, Rs = 0, R1 = R2 = 0.455 Ω; regime from kc = 0.0318 (RL = 6 Ω, Rs = 0).
k, M: closed form vs Neumann agree to ≤ 0.05 % (0.5–15 cm).
(a) Model chain. (b) PL (W) vs f (kHz) at 2, 5, 10 cm, RL = 6 Ω; markers: LTspice; dotted lines: light-load f± at 5 cm. (c) i1, i2 (A) vs t (µs), 5 cm: i2 lags i1 by 90°. Read k only from light-load peaks.
Key findings
• Q = 118.3: ηmax = 96.8 % at 1 cm, 85.9 % at 5 cm (RL,opt = 6.0 Ω), 57.2 % at 10 cm.
• Max η ≠ max power: at 5 cm, RL,opt = 6.0 Ω, but RL = 79.1 Ω gives the most power.
Limitations
• Range: M ∝ 1/d3 only for d ≫ a (log-log slope −2.1 at 8–10 cm, −2.97 at 50–100 cm).
• AC loss: Rdc 0.13 → 0.455 Ω (skin 0.269, prox. 0.136, ESR 0.035, joints 0.015); range 0.38–0.48 Ω.
• Misalignment (3 cm): η = 91.1 / 88.8 / 84.2 % at Δx = 2 / 3 / 4 cm; M = 0 at 8.22 cm, then M < 0.
• Al plate 5 mm behind coil 2: k −56.4 %, R2 +178 mΩ, L2 −51 %; ferrite: k +34.5 %. η (3 cm): 92.5 → 24.0 % (63.9 % with C2 retuned).
• Stress (Rs = 0): VC1 44.8 / 314 V pk at 5 / 10 cm; I1 ≤ 11.0 A pk, 27.5 W (50 Ω source: 0.1 A). Field: 82.3 µT rms at z = 0, < 27 µT rms (ICNIRP 2010) beyond 4.7 cm, < 1.84 beyond 15.4 cm.
Future work: build and measure a prototype; ferrite backing; adaptive frequency tuning [2].
[1] A. Kurs et al., Science, vol. 317, no. 5834, pp. 83–86, 2007.
[2] A. P. Sample, D. A. Meyer, and J. R. Smith, IEEE Trans. Ind. Electron., vol. 58, no. 2, pp. 544–554, 2011.
[3] S. Y. R. Hui, W. Zhong, and C. K. Lee, IEEE Trans. Power Electron., vol. 29, no. 9, pp. 4500–4511, 2014.
[4] R. K. Shevgaonkar, Electromagnetic Waves. New Delhi: Tata McGraw-Hill, 2006.